## Slide 2
MODELOS E ESTRUTURA DE COMPUTADORES
PROF. SANDRO A. FERRAZ, PhD
SISTEMA DE INFORMAÇÃO

## Slide 3
Escrevendo o programa do arduino

## Slide 4
Entendendo os movimentos do robô

## Slide 5
Entendendo os movimentos do robô
Frente

## Slide 6
Entendendo os movimentos do robô
Trás

## Slide 7
Entendendo os movimentos do robô
Esquerda

## Slide 8
Entendendo os movimentos do robô
Direita

## Slide 9
Entendendo os movimentos do robô
Pino | 6 | 9 | Motor
Valor escrito | 0 | 0 | Parado
Valor escrito | 1 - 255 | 0 | Para frente
Valor escrito | 0 | 1 - 255 | Para trás
No código:
analogWrite (3, 0);
analogWrite (5, 0);
Motor direito parado.
Efeito:
Pino | 3 | 5 | Motor
Valor escrito | 0 | 0 | Parado
Valor escrito | 1 - 255 | 0 | Para frente
Valor escrito | 0 | 1 - 255 | Para trás
analogWrite (3, 128);
analogWrite (5, 0);
Motor direito para frente com aproximadamente metade da potência.
analogWrite (3, 0);
analogWrite (5, 128);
Motor direito para trás com aproximadamente metade da potência.

## Slide 10
Entendendo os movimentos do robô
Pino | 6 | 9 | Motor
Valor escrito | 0 | 0 | Parado
Valor escrito | 1 - 255 | 0 | Para frente
Valor escrito | 0 | 1 - 255 | Para trás
No código:
analogWrite (3, 0);
analogWrite (5, 0);
Motor direito parado.
Efeito:
Pino | 3 | 5 | Motor
Valor escrito | 0 | 0 | Parado
Valor escrito | 1 - 255 | 0 | Para frente
Valor escrito | 0 | 1 - 255 | Para trás
analogWrite (3, 128);
analogWrite (5, 0);
Motor direito para frente com aproximadamente metade da potência.
analogWrite (3, 0);
analogWrite (5, 128);
Motor direito para trás com aproximadamente metade da potência.

## Slide 11
Entendendo os movimentos do robô
Pino | 6 | 9 | Motor
Valor escrito | 0 | 0 | Parado
Valor escrito | 1 - 255 | 0 | Para frente
Valor escrito | 0 | 1 - 255 | Para trás
No código:
analogWrite (3, 0);
analogWrite (5, 0);
Motor direito parado.
Efeito:
Pino | 3 | 5 | Motor
Valor escrito | 0 | 0 | Parado
Valor escrito | 1 - 255 | 0 | Para frente
Valor escrito | 0 | 1 - 255 | Para trás
analogWrite (3, 128);
analogWrite (5, 0);
Motor direito para frente com aproximadamente metade da potência.
analogWrite (3, 0);
analogWrite (5, 128);
Motor direito para trás com aproximadamente metade da potência.

## Slide 12
Fluxograma do programa

## Slide 13
Abrindo o Arduino IDE

## Slide 14
Arduino IDE

## Slide 15
Arduino IDE
char data_serial;
void setup() {
void loop() {

## Slide 16
Arduino IDE
char data_serial;
void setup() {
Serial.begin (9600);}
void loop() {

## Slide 17
Arduino IDE
char data_serial;
void setup() {
Serial.begin (9600);}
void loop() {
if (Serial.available () > 0){

## Slide 18
Arduino IDE
char data_serial;
void setup() {
Serial.begin (9600);}
void loop() {
if (Serial.available () > 0){
data_serial = Serial.read();

## Slide 19
Arduino IDE
char data_serial;
void setup() {
Serial.begin (9600);}
void loop() {
if (Serial.available () > 0){
data_serial = Serial.read();
if (data_serial == 'u'){

## Slide 20
Arduino IDE
char data_serial;
void setup() {
Serial.begin (9600);}
void loop() {
if (Serial.available () > 0){
data_serial = Serial.read();
if (data_serial == 'u'){
analogWrite(6, 180);

## Slide 21
Arduino IDE
char data_serial;
void setup() {
Serial.begin (9600);}
void loop() {
if (Serial.available () > 0){
data_serial = Serial.read();
if (data_serial == 'u'){
analogWrite(6, 180);
analogWrite(9, 0);

## Slide 22
Arduino IDE
char data_serial;
void setup() {
Serial.begin (9600);}
void loop() {
if (Serial.available () > 0){
data_serial = Serial.read();
if (data_serial == 'u'){
analogWrite(6, 180);
analogWrite(9, 0);
analogWrite(3, 180);

## Slide 23
Arduino IDE
char data_serial;
void setup() {
Serial.begin (9600);}
void loop() {
if (Serial.available () > 0){
data_serial = Serial.read();
if (data_serial == 'u'){
analogWrite(6, 180);
analogWrite(9, 0);
analogWrite(3, 180);
analogWrite(5, 0);}

## Slide 24
Arduino IDE
void setup() {
Serial.begin (9600);}
void loop() {
if (Serial.available () > 0){
data_serial = Serial.read();
if (data_serial == 'u'){
analogWrite(6, 180);
analogWrite(9, 0);
analogWrite(3, 180);
analogWrite(5, 0);}

## Slide 25
Arduino IDE
void setup() {
Serial.begin (9600);}
void loop() {
if (Serial.available () > 0){
data_serial = Serial.read();
if (data_serial == 'u'){
analogWrite(6, 180);
analogWrite(9, 0);
analogWrite(3, 180);
analogWrite(5, 0);}
if (data_serial == 'd'){

## Slide 26
Arduino IDE
Serial.begin (9600);}
void loop() {
if (Serial.available () > 0){
data_serial = Serial.read();
if (data_serial == 'u'){
analogWrite(6, 180);
analogWrite(9, 0);
analogWrite(3, 180);
analogWrite(5, 0);}
if (data_serial == 'd'){
analogWrite(6, 0);

## Slide 27
Arduino IDE
void loop() {
if (Serial.available () > 0){
data_serial = Serial.read();
if (data_serial == 'u'){
analogWrite(6, 180);
analogWrite(9, 0);
analogWrite(3, 180);
analogWrite(5, 0);}
if (data_serial == 'd'){
analogWrite(6, 0);
analogWrite(9, 180);

## Slide 28
Arduino IDE
if (Serial.available () > 0){
data_serial = Serial.read();
if (data_serial == 'u'){
analogWrite(6, 180);
analogWrite(9, 0);
analogWrite(3, 180);
analogWrite(5, 0);}
if (data_serial == 'd'){
analogWrite(6, 0);
analogWrite(9, 180);
analogWrite(3, 0);

## Slide 29
Arduino IDE
if (Serial.available () > 0){
data_serial = Serial.read();
if (data_serial == 'u'){
analogWrite(6, 180);
analogWrite(9, 0);
analogWrite(3, 180);
analogWrite(5, 0);}
if (data_serial == 'd'){
analogWrite(6, 0);
analogWrite(9, 180);
analogWrite(3, 0);
analogWrite(5, 180);}

## Slide 30
Arduino IDE
data_serial = Serial.read();
if (data_serial == 'u'){
analogWrite(6, 180);
analogWrite(9, 0);
analogWrite(3, 180);
analogWrite(5, 0);}
if (data_serial == 'd'){
analogWrite(6, 0);
analogWrite(9, 180);
analogWrite(3, 0);
analogWrite(5, 180);}

## Slide 31
Arduino IDE
if (data_serial == 'u'){
analogWrite(6, 180);
analogWrite(9, 0);
analogWrite(3, 180);
analogWrite(5, 0);}
if (data_serial == 'd'){
analogWrite(6, 0);
analogWrite(9, 180);
analogWrite(3, 0);
analogWrite(5, 180);}
if (data_serial == 'r'){

## Slide 32
Arduino IDE
analogWrite(6, 180);
analogWrite(9, 0);
analogWrite(3, 180);
analogWrite(5, 0);}
if (data_serial == 'd'){
analogWrite(6, 0);
analogWrite(9, 180);
analogWrite(3, 0);
analogWrite(5, 180);}
if (data_serial == 'r'){
analogWrite(6, 0);

## Slide 33
Arduino IDE
analogWrite(6, 180);
analogWrite(9, 0);
analogWrite(3, 180);
analogWrite(5, 0);}
if (data_serial == 'd'){
analogWrite(6, 0);
analogWrite(9, 180);
analogWrite(3, 0);
analogWrite(5, 180);}
if (data_serial == 'r'){
analogWrite(6, 0);
analogWrite(9, 180);

## Slide 34
Arduino IDE
analogWrite(9, 0);
analogWrite(3, 180);
analogWrite(5, 0);}
if (data_serial == 'd'){
analogWrite(6, 0);
analogWrite(9, 180);
analogWrite(3, 0);
analogWrite(5, 180);}
if (data_serial == 'r'){
analogWrite(6, 0);
analogWrite(9, 180);
analogWrite(3, 180);

## Slide 35
Arduino IDE
analogWrite(3, 180);
analogWrite(5, 0);}
if (data_serial == 'd'){
analogWrite(6, 0);
analogWrite(9, 180);
analogWrite(3, 0);
analogWrite(5, 180);}
if (data_serial == 'r'){
analogWrite(6, 0);
analogWrite(9, 180);
analogWrite(3, 180);
analogWrite(5, 0);}

## Slide 36
Arduino IDE
analogWrite(5, 0);}
if (data_serial == 'd'){
analogWrite(6, 0);
analogWrite(9, 180);
analogWrite(3, 0);
analogWrite(5, 180);}
if (data_serial == 'r'){
analogWrite(6, 0);
analogWrite(9, 180);
analogWrite(3, 180);
analogWrite(5, 0);}

## Slide 37
Arduino IDE
if (data_serial == 'd'){
analogWrite(6, 0);
analogWrite(9, 180);
analogWrite(3, 0);
analogWrite(5, 180);}
if (data_serial == 'r'){
analogWrite(6, 0);
analogWrite(9, 180);
analogWrite(3, 180);
analogWrite(5, 0);}
if (data_serial == 'l'){

## Slide 38
Arduino IDE
if (data_serial == 'd'){
analogWrite(6, 0);
analogWrite(9, 180);
analogWrite(3, 0);
analogWrite(5, 180);}
if (data_serial == 'r'){
analogWrite(6, 0);
analogWrite(9, 180);
analogWrite(3, 180);
analogWrite(5, 0);}
if (data_serial == 'l'){
analogWrite(6, 180);

## Slide 39
Arduino IDE
analogWrite(9, 180);
analogWrite(3, 0);
analogWrite(5, 180);}
if (data_serial == 'r'){
analogWrite(6, 0);
analogWrite(9, 180);
analogWrite(3, 180);
analogWrite(5, 0);}
if (data_serial == 'l'){
analogWrite(6, 180);
analogWrite(9, 0);

## Slide 40
Arduino IDE
analogWrite(9, 180);
analogWrite(3, 0);
analogWrite(5, 180);}
if (data_serial == 'r'){
analogWrite(6, 0);
analogWrite(9, 180);
analogWrite(3, 180);
analogWrite(5, 0);}
if (data_serial == 'l'){
analogWrite(6, 180);
analogWrite(9, 0);
analogWrite(3, 0);

## Slide 41
Arduino IDE
analogWrite(3, 0);
analogWrite(5, 180);}
if (data_serial == 'r'){
analogWrite(6, 0);
analogWrite(9, 180);
analogWrite(3, 180);
analogWrite(5, 0);}
if (data_serial == 'l'){
analogWrite(6, 180);
analogWrite(9, 0);
analogWrite(3, 0);
analogWrite(5, 180);}

## Slide 42
Arduino IDE
analogWrite(5, 180);}
if (data_serial == 'r'){
analogWrite(6, 0);
analogWrite(9, 180);
analogWrite(3, 180);
analogWrite(5, 0);}
if (data_serial == 'l'){
analogWrite(6, 180);
analogWrite(9, 0);
analogWrite(3, 0);
analogWrite(5, 180);}

## Slide 43
Arduino IDE
if (data_serial == 'r'){
analogWrite(6, 0);
analogWrite(9, 180);
analogWrite(3, 180);
analogWrite(5, 0);}
if (data_serial == 'l'){
analogWrite(6, 180);
analogWrite(9, 0);
analogWrite(3, 0);
analogWrite(5, 180);}
if (data_serial == 's'){

## Slide 44
Arduino IDE
if (data_serial == 'r'){
analogWrite(6, 0);
analogWrite(9, 180);
analogWrite(3, 180);
analogWrite(5, 0);}
if (data_serial == 'l'){
analogWrite(6, 180);
analogWrite(9, 0);
analogWrite(3, 0);
analogWrite(5, 180);}
if (data_serial == 's'){
analogWrite(6, 0);

## Slide 45
Arduino IDE
analogWrite(6, 0);
analogWrite(9, 180);
analogWrite(3, 180);
analogWrite(5, 0);}
if (data_serial == 'l'){
analogWrite(6, 180);
analogWrite(9, 0);
analogWrite(3, 0);
analogWrite(5, 180);}
if (data_serial == 's'){
analogWrite(6, 0);
analogWrite(9, 0);

## Slide 46
Arduino IDE
analogWrite(9, 180);
analogWrite(3, 180);
analogWrite(5, 0);}
if (data_serial == 'l'){
analogWrite(6, 180);
analogWrite(9, 0);
analogWrite(3, 0);
analogWrite(5, 180);}
if (data_serial == 's'){
analogWrite(6, 0);
analogWrite(9, 0);
analogWrite(3, 0);

## Slide 47
Arduino IDE
analogWrite(3, 180);
analogWrite(5, 0);}
if (data_serial == 'l'){
analogWrite(6, 180);
analogWrite(9, 0);
analogWrite(3, 0);
analogWrite(5, 180);}
if (data_serial == 's'){
analogWrite(6, 0);
analogWrite(9, 0);
analogWrite(3, 0);
analogWrite(5, 0);}}}

## Slide 48
Passando o programa para o arduino

## Slide 49
Ligando o Arduino no computador

## Slide 50
Passando o programa para o Arduino

## Slide 51
Passando o programa para o Arduino

## Slide 53
Copyright © 2021 Prof. Sandro A. Ferraz
Todos direitos reservados. Reprodução ou divulgação total ou parcial deste documento é expressamente proíbido sem o consentimento formal, por escrito, do Professor (autor).